## Slide 1: 1. THEORETICAL FOUNDATION
1 / 9
Problem: dam break is a two-phase (water + air) flow. A water column is released instantly and collapses under gravity, so the region occupied by water is unknown and changes every step.
NAVIER-STOKES (MOMENTUM, MIXTURE)
ρ[∂u/∂t + (u·∇)u] = −∇p + ∇·[μ(∇u + ∇u^T)] + ρg
CONTINUITY (MASS)
∇ · u = 0
MIXTURE PROPERTIES (LINEAR BLEND OF Α)
ρ = α·ρ_water + (1−α)·ρ_air
μ = α·μ_water + (1−α)·μ_air
VOF method: a fixed grid spans both fluids. α = water volume / cell volume: α = 1 water, α = 0 air, 0 < α < 1 interface cell. ρ and μ are recomputed from α every step.

## Slide 2: 2. INTERFACE TRANSPORT
2 / 9
Α TRANSPORT: NO DIFFUSION, NO SOURCE
∂α/∂t + u·∇α = 0
equivalent to ∂α/∂t + ∇·(αu) = 0 because ∇·u = 0 (conservative form)
SCHEME | WHAT IT DOES | TRADE-OFF
Plain upwind | α treated like any other scalar | Easy, but interface smears
Donor-acceptor (USED) | Blends upwind/downwind by interface orientation and donor fullness | Sharp without geometry; needs CFL < 1
PLIC | Straight-line interface per cell, exact geometric fluxes | Sharpest; many edge cases
Van Leer | Flux limiter for momentum, not for α | High order when smooth, bounded at jumps

## Slide 3: 3. TIME STEP: CHORIN PROJECTION
3 / 9
1. PREDICTOR (NO PRESSURE)
u* = u + Δt·[ −(u·∇)u
+ (1/ρ)∇·(μ∇u) + g ]
2. PRESSURE POISSON
∇·((1/ρ)∇p)
= (1/Δt) ∇·u*
3. PROJECTION
u(n+1) = u* − (Δt/ρ)∇p
so that ∇·u(n+1) = 0
4. Advect α with the corrected velocity (donor-acceptor), then clip α to [0, 1].
5. Recompute ρ and μ from α; repeat with a CFL-limited Δt.
Why split? u* is where the water wants to go from gravity, momentum and viscosity alone. The Poisson solve finds the pressure that removes the divergence of u*; the projection applies it.

## Slide 4: 4. DENSITY RATIO AND PRESSURE SOLVE
4 / 9
FLUID | DENSITY (ρ) | KINEMATIC VISCOSITY (ν) | RATIO
Water | 998.0 kg/m³ | 1.00e-6 m²/s | ~832× (ρ)
Air | 1.20 kg/m³ | 1.48e-5 m²/s | 
WHY IT IS ILL-CONDITIONED
The coefficient 1/ρ jumps ~832× across a single interface cell, so the Poisson matrix entries span about three orders of magnitude and plain CG converges slowly.
FIX: IC(0)-PRECONDITIONED CG
2450 → 112 iterations
18.5 → 2.1 ms per step; scaling O(N^1.5) → O(N^1.2)
Matrix assembly: the 5-point Laplacian must treat fluid and empty cells carefully to stay symmetric positive definite.

## Slide 5: 5. DAM-BREAK THEORY: RITTER
5 / 9
WATER AT REST (h = H)
−c0·t
gate x=0
2c0·t
SHALLOW WATER (SAINT-VENANT)
h_t + (h·u)_x = 0
u_t + u·u_x + g·h_x = 0
RITTER SOLUTION, C0 = √(GH)
u = (2/3)(c0 + x/t)
h = (2·c0 − x/t)² / (9g)
for −c0·t ≤ x ≤ 2·c0·t
WHAT IT PREDICTS (VALID FOR T < L0/C0, BEFORE REFLECTION OFF THE BACK WALL)
Front speed 2√(gH) with zero depth. At the gate: h = 4H/9, u = c (Fr = 1), constant discharge q = (8/27)·√g·H^1.5.

## Slide 6: 6. REALITY CHECK: FRICTION AND SCALING
6 / 9
AVERAGE FRONT SPEED v/√(gH), t* > 1
Chart: 
| Ritter | Lobovský 300 | Lobovský 600 | M&M 57 | M&M 114 | Dressler 110 | Hu | Koshizuka
v/√(gH) | 2 | 1.56 | 1.34 | 1.48 | 1.69 | 1.7 | 1.21 | 1.3
Source: Lobovský et al., Table 1. M&M = Martin & Moyce; numbers after names are H in mm.
FRICTION (DRESSLER, WHITHAM)
Blunt front, vertical tangent, finite depth. Slower than 2√(gH).
LAB SCALE, H = 300 MM
Re = 3.8e6, We = 1.64e5, Fr = 1
Large We: surface tension negligible
EARLY TIMES, T* < 1
Not hydrostatic; gate removal (3.5–4.5 m/s) matters.

## Slide 7: 7. VALIDATION
7 / 9
SOURCE | LENGTH | TIME
Martin & Moyce | initial width a | T = t√(g/a)
Lobovský | depth H | t* = t√(g/H)
This solver | L0 | T* = t√(g/L0)
EARLY-TIME CHECK (RITTER)
X* = 1 + 2·T*
front starts at x/L0 = 1, then moves at 2√(gH); square column
Match the axis convention of the data you overlay before comparing curves.
ACCEPTANCE CHECKS
∫α dV stays within a stated tolerance (live readout)
Front X*(T*) vs Martin & Moyce data
Front stays below Ritter: 1 + 2T*
Late front speed about 1.1–1.75 √(gH)
∇·u ≈ 0 after every projection
Error shrinks under grid and Δt refinement

## Slide 8: 8. IMPACT PRESSURE AT A WALL
8 / 9
MEDIAN PEAK, 3 MM ABOVE BED
≈ 3 × ρgH
97.5th percentile ≈ 4.5×
P / ΡV², MEASURED
1.25
vs 0.5 for a steady impinging jet
REPEATED RUNS PER FILL HEIGHT
100
peak pressure is a random variable
Time scales: rise 1.5–4.5 ms, decay about 10× longer. Impulse ∫P dt ≈ ½ × peak × impact time (within about 25%).
Scaling: lowest-sensor peak ∝ H (Froude: P ~ ρgH); higher sensors are not linear in H.
For your solver: incompressible VOF gives a sharp, grid-dependent spike. Compare arrival time and impulse with the median and 95% band, not one peak.

## Slide 9: 9. SCOPE FOR IMPROVEMENT
9 / 9
HIGHER-ORDER INTERFACE TRACKING
Replace donor-acceptor with PLIC for a continuous, sharp geometric interface reconstruction.
HARDWARE ACCELERATION
Port grid sweeps and the Poisson solver to WebGPU compute shaders; scale to millions of cells and 3D.
PHYSICS GAPS
Air compressibility and entrapment at impact, wet-bed jets, and turbulence at Re ~ 1e6 on an under-resolved grid.
3D EFFECTS
The lab flow stops being 2D at H = 600 mm, which a 2D solver cannot show.